## Slide 1: Navx:
Path planning for a tactical unmanned ground vehicle
Alvin O’Garro
Jacob Jeong
Antony Samuel
Kartik sastry

## Slide 2: Introduction
Objective:
High-level path-planning for an existing mobile robot, the Tactical Unmanned Ground Vehicle (TUGV)
  Input: High-resolution LIDAR point-cloud data with point classification
  Output: A set of “waypoints” that the TUGV can navigate
  Current Strategy: Graph-based
Motivation:
Mission Planning
Intelligence, Surveillance, and Reconnaissance (ISR)
Area Scanning
Background:
Two major Components:
  Mapping/Representation (discrete vs. continuous)
  Planning Algorithms (coupled with representation)
Emergency Situation Response
Warehousing/Material Handling

## Slide 3: Project Description and Goals
Qualitative Goals:
Construct a graph model of a geographic area and assign edge weights per information extracted from LIDAR data and fundamental vehicle limitations.
Compute the single-source, least-cost path to a specified destination.
Translate the result of the graph search into a sequence of waypoints; Transmit the waypoints to the TUGV.
Specifications:
Base Station Parameter | Minimum Requirements
Clock Speed | 2.0 GHz
RAM | 8 GB
Disk/Flash Memory | 256 GB
I/O | 802.11n Wi-Fi USB Serial Interface

## Slide 4: Design Approach Details
Design Approach
Global Path planning on base station
Discrete map representation
Graph-based search algorithm
Waypoints to TUGV
Codes and Standards
LAS, Serial, Wifi
Constraints, Alternatives, Tradeoffs
Preprocessed vs raw LiDAR
Base Station Computation Limits
Data Resolution

## Slide 5: Schedule/Milestones
Documentation/Website maintenance
3 main tasks:
  Data Acquisition, Preprocessing
  Developing Representation
  Implementing Path Planning Algorithm

## Slide 6: Schedule/Milestones
Week 2-5: Data acquisition, preprocessing (Jacob, Antony)
Week 2-7: Develop code for data representation (Kartik)
Week 2-9: Implementing path planning algorithm (Alvin)
Week 2-4: Integrating with Team B
Week 10-11: Output generation
Design reviews
  Critical design review: Week 8
  Technical readiness review: Week 12
Week 14-15: Testing + Expo prep

## Slide 7: Project Demonstration
Data Input
Processing Checkpoints
Waypoints Output
Final Verification
Pre-Processed LiDAR
Visualization of Step #1
Visualization of Step #2
…
Waypoints Visualization overlaid on map

## Slide 8: Marketing analysis
Harris Corporation is an American Technology Company, Defense Contractor, and IT services group
With a single customers, our product captures its intended market by following requirements requested by the direct customer
Working with Mr. McGonagle to establish and read all technical specifications

## Slide 9: Cost Analysis
Deliverables are all software-related and don’t have any hardware-related costs
Cost is solely a function of software salary
COST | AMOUNT (USD)
Alvin O’Garro Salary | $6587.20
Jacob Jeong Salary | $6587.20
Antony Samuel Salary | $6587.20
Kartik Sastry Salary | $6587.20
TOTAL | $26,348.80

## Slide 10: Next Steps
Coordinating GIS requirements with Mr. McGonagle
Experimentation/Discussion of mapping and path planning options
Detailed, system level block diagram for software